| Activity Details |
| --- |
| Work Activity: | Loading and unloading of plant via tilt tray |
| Address of activity |  | Project/Client Name: |  |
| Commencement date |  | Duration of works |  |

| Worker Details |
| --- |
| Supervisor of the Work* |  | Signature: |  | Qualifications: |  |
| Authorising Jaybro/Orange Hire Person# |  | Signature: |  | Position: |  |
| Number of workers used onsite | 1 | Primary contact number |  | Sub-Contractor Name |  |
| SWMS Preparation | Name | Date |
| SWMS prepared by: | Scott Montgomery |  | Reviewed 02/09/2016 |
| Worker(s) who have had input into the development of this SWMS | Mark Johnson | Date:31/03/2015 |
|  |  | Date: |
| Associated SWMS (e.g. Subcontractors SWMS) |  |

## *- Responsible for providing site specific training; Implementing & monitoring implementation of this SWMS and conducting inspection

# - Responsible for ensuring SWMS are developed, consulted upon, distributed, returned, filed and all other WHS tasks completed including inspections

| Personal Protective Equipment | Site Specific Requirements / Notes |
| --- | --- |
| Safety boots Lace up | High Visible clothing | Eye protection | Gloves | Hard Hat | Hearing protection | Special PPE__________ Crew to be inducted into SWMS. Crew to be advised on onsite risks and hazards |
| Mandatory | Mandatory |  |  |  |  |  |
| HRW & Other Licences Required | Training Required | Permits/Approvals |
| Dogman Rigging basic Rigging Int. Rigging Adv WP (>11m) Traffic Control MR/HR truck* HC/MC truck* LF/LO fork *Dependant on truck type Other_______ Other _______ Crane License C2 C6 C1 C0 CV (>10mT) CN | Construction Industry General Induction Site Induction ( This SWMS SDS Confined Space Manual Handling Verification of Competency for plant Trade Certificate | Excavation Other ____________ Working at Height Other ____________ Hot works Confined Space Traffic Management Other ____________ |
| High Risk Work Check |
| Note which high risk work activities are involved in this project |
| Risk of falls from greater than 2 meters | Work in an area with movement of powered mobile plant Work on a telecommunications tower | Temporary load-bearing support structures Demolition of a load-bearing structure |
| Work on, in or adjacent to road, rail shipping or other major traffic corridor | Work in or near shaft or trench with an excavated depth greater than 1.5m or a in a tunnel | Use of Explosives Likely to involve disturbing asbestos |
| Work on or near pressurized gas pipes or mains | Work on or near chemical, fuel or refrigerant lines Work in confined spaces | Work on or near energized electrical installations or services |
| Work with tilt up or pre-cast concrete Diving work | Work in or near a drowning risk Work in areas with artificial extremes of temperature | Work in an area with contaminated or flammable atmosphere |
| Emergency Planning (tick or add as applicable and attach plan or details as required) |
| First Aid kit |
| 9kg Fire Extinguisher |
| Radio | Channel: |

| Protective Barriers (tick or add as applicable) |
| --- |
| List warning signs, protective barriers and equipment to be used on this site: |
| PROTECTIVE BARRIERS: Bollards/Cones Edge protection Tape __Traffic Control______________________ | SIGNS: Danger plant in use Stop/Slow baton Other ______________________ | Other: Warning lights, reversing alarms |
| Substances to be brought on to site Note: Any Hazardous Substance must have a valid Safety Data Sheet |
| Product | SDS Attached | Product | SDS Attached |
| E.g. Diesel fuel |  |  |  |
| Plant and Equipment (tick or add as applicable) | Note: All servicing MUST be in accordance with manufacturers recommendations |
| Plant and Equipment to be used on this site? | List inspections and maintenance requirements and attach evidence to this SWMS |
| Vehicle | Visual inspection |
| Excavator | Visual inspection |
| Hoses | Visual inspection of hoses, clamps and connectors |
| Electrical leads | Visual inspection Tagged and tested |
| Welding Equipment | Visual inspection Tagged and tested Hot work permit |
| Other | Visual inspection ___________ |
| Other | Visual inspection |

## Risk Matrix

| Step 1: Determine Likelihood What is the possibility that the event will occur? |  | Step 2: Determine Consequence What will be the expected outcome? |
| --- | --- | --- |
| Likelihood | Criteria |  | Level of Effect: | Example of each level: | Level of Effect: | Example of each level: |
| Almost certain | Expected in most circumstances. |  | Minor | First Aid treatment only; no lost time injury | Negligible Discharge | Minor clean up necessary |
| Likely | Will probably occur in most circumstances |  | Moderate | Medical treatment; serious injuries, temporary partial disability; lost time injury < 7 days | Moderate Breach | Spill kit deployed, drains and gutters secured; Workzone personnel and site contact notified |
| Possible | Might occur at some time |  | Major | Hospital admittance; extensive injuries; lost time injury > 7 days; Permanent Total Disability injury; death | Major Breach of Environmental Statutes | Fire brigade services required for clean-up; Public diverted or evacuated. Principal Contractor notified. |
| Unlikely | Could occur at some time |  | Catastrophic | Multiple Permanent Total Disability injuries; multiple deaths | Shutdown of Project due to Environmental Breach | Site shutdown and emergency services required; evacuation of personnel and public |

|  | Step 3: Determine the risk score Using the above steps, determine the risk score? |  | Step 4: Record risk score on worksheet (Note – Risk scores are a subjective value and should only be used for comparison and to engender discussion.) |
| --- | --- | --- | --- |
|  | Consequences |  |  |
|  | People | Minor | Moderate | Major | Catastrophic |  | Score | Action |
|  | Environment | Negligible Spill/effect | Moderate Breach of Environmental law | Major Breach of Environmental law | Shutdown of Project due to Environmental Breach |  | 4 Severe | DO NOT PROCCED. Requires immediate attention. Introduce further high-level controls to lower the risk level. Re-assess before proceeding. |
| Likelihood | Almost certain | 3 High | 4 Severe | 4 Severe | 4 Severe |  | 3 High | Review before commencing work. Introduce new controls and/or maintain high-level controls to lower the risk level. Monitor frequently to ensure control measures are working. |
|  | Likely | 3 High | 3 High | 4 Severe | 4 Severe |  | 2 Moderate | Maintain control measures. Proceed with work. Monitor and review regularly, and if any equipment/people/materials/work processes or procedures change. |
|  | Possible | 2 Moderate | 3 High | 4 Severe | 4 Severe |  | 1 Low | Record and monitor. Proceed with work. Review regularly, and if any equipment/people/materials/work processes or procedures change. |
|  | Unlikely | 1 Low | 2 Moderate | 3 High | 4 Severe |  |  |  |
| ACTIVITY Break the job into steps What are you doing? | Hazards and Risks What harm can occur to workers or others | UNTREATED RISK RANKING (4S, 3H, 2M or 1L) | CONTROLS What are you going to do to carry out the work safely? (Apply the hierarchy of control) | RISIDUAL RISK RANKING (4S, 3H, 2M or 1L) | PERSON RESPONSIBLE for implementation of the controls |
| Step 1. Site access |  |
| Arrival onsite | Unaware of site safety rules, hazards and instruction | 4S | All members of the crew will need to be: site inducted (where appropriate); trained in this SWMS; involved in the Work Site Inspection for the work Make sure you are aware of the site’s emergency procedures. If at any time you are unsure or have questions – Speak Up & ask your Supervisor and/or site manager for advice. Assess weather conditions and adjust work accordingly Locate area where item is being delivered and assess the area. Discuss truck bed access with site supervisor and make adjustments as necessary Assess hazards before commencement. Check for: Drains, gutters and other water services Pits, pot holes and ditches Debris that may affect ramp/tilt tray other mobile equipment moving within the working area | 2M | Supervisor |
| Pre Job Risk Assessment |  | 4S | You must inspect the site and complete the Work Site Inspection form (last page of SWMS) before commencing work activity. Do not commence work until you are satisfied the job is safe! | 1L | Supervisor |

| Step 2. Arriving onsite |
| --- |
| Position truck onsite | Driving or parking in an unauthorised area | 2M | Call or radio ahead to find out which gate or location you should deliver the plant to | 1L | Supervisor |
|  | Overhead wires, services, obstructions or structures | 3H | LOOK UP AND LIVE – Inspect the area for overhead wires, services, structure or obstructions Do not unload under overhead wires, structures, services or obstructions to the unloading | 2M | Supervisor |
|  | Hit by moving plant Hit my moving vehicles | 4S | Park in areas assigned Unload vehicle off roadways where possible Where unloading on a roadway is required, use traffic cones at least 60cm from side of vehicle to warn traffic. Follow road safety laws at all times. PPE to be worn, steel capped boots and high visibility garments | 2M | Supervisor |
| Step 3. Preparing plant for unloading |
| Performing duties near roadways or mobile plant | Hit by moving vehicles/plant | 3H | Check constantly for changing hazards while working Monitor work position at all times. Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure –such as plant rollover) No work is conducted in established “no go zones” Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan where required Never assume you have right of way. Make visual and verbal contact with plant operator as required. Avoid performing work on roadway directly where possible Use traffic cones and signage where available | 2M | Supervisor |
| Fitting ramp | Manual Handling | 3H | Adopt correct manual handling practices, bring loads in close to the body, keep back straight and lift with legs not the back. Two person lift where possible | 2M | Supervisor |
|  | Fall from truck tray | 3H | 3 points of contact at all times when access the truck bed When ramps are installed, access via ramp Care must be taken in wet condition Safety footwear must be worn | 2M | Supervisor |
|  | Crush, pinch hazard | 2M | Gloves are to be worn by the installer of ramps Fingers are to be kept clear of pinch or nip points of ramps and stabilisers | 1L | Supervisor |
|  | Slips, trips and falls | 3H | Inspect the area for slips and trip hazards- Reo, timber, debris, broken or uneven ground are often found on construction sites. Clear these were possible. Look out for steps, gutters and other obstacles especially where they may affect using remote/tilt operation | 2M | Supervisor |
|  | Tipping or roll over of plant | 3H | Park on solid, dry ground away from ravines, ditches or trenches Detach and secure all chains and straps Ramps must be on solid footing Check locking mechanisms are in good condition without cracks, distortion or damage Locking mechanisms must be in place Attachment must be facing upward when unloading Lift attachments off truck bed | 2M | Supervisor |
| Operating tilt tray | Tipping or roll over of plant | 3H | Deploy stabilizers where fitted Detach and secure all chains and straps Park on solid, dry ground away from ravines, ditches or trenches Tilt tray on solid footing Air bags dumped where fitted Lift attachments off truck bed Leave winch attached when using winch and drive technique Attachment must be facing upward when unloading | 2M | Supervisor |
|  | Overhead wires and services | 3H | Look up and Live! Inspect area before moving tilt tray; look out for overhead wires and electrical services including lights Minimum clearance from overhead services to be maintained at all times with a spotter utilized when required | 2M | Supervisor |
|  | Fall from cabin | 3H | 3 points of contact at all times when access the truck bed and cabin Care must be taken in wet condition Safety footwear must be worn Fit seat belt when in plant cabin | 2M | Supervisor |
| Step 4. Unloading plant |
| Moving plant from the truck bed | Failure of plant | 3H | Inspect plant before use Operator must be competent in the operation of the plant Cease operation if plant makes unusual noise, vibration or warning lights are illuminated Tag out and report issue to site contact and Orange hire Do not refuel plant. Report to site personnel or orange hire | 2M | Supervisor |
|  | Tipping or roll over of plant | 3H | Plant is to move forward only, do not turn Move at a very slow pace Float attachment, close to ground/surface Leave winch attached when using winch and drive technique – maintain tension on the line Use a spotter where required | 2M | Supervisor |
|  | Damage to surfaces | 2M | Inspect area of travel and be sure the surface is capable of taking the weight of the plant without damage | 1L | Supervisor |
|  | Damage to equipment | 2M | Clear the tray of debris or material including chains and straps Double check that attachments are securely locked in Unattached/extra buckets are firmly in the fixed bucket Do not place other attachments onto truck bed until plant is in place and secured | 1L | Supervisor |
|  | Struck by moving plant | 4S | Establish and maintain an exclusion zone use a spotter where required | 2M | Supervisor |
| Driving to parking location | Hitting other vehicles, persons or property | 3H | Follow site safety rules and traffic management. Inspect area before moving plant; look out for: overhead wires, pipes, vegetation, drains, gutters and water services, pits holes, ditches and structures. Look out for traffic thoroughfares and pedestrian walkways Monitor direction of travel and surroundings at all times. Ensure: Do not drive behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure –such as plant rollover) Stop work immediately if pedestrians enter “no go zones” Alertness at all times. Listen for: Reversing alarms/beepers Calls from site workers Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Make visual and verbal contact with other plant operators and pedestrians as required. Ensure clearance from structures Never drive over or alongside trenches, they may collapse | 2M | Supervisor |
|  | Overhead wires and services | 3H | Look up and Live! Inspect area before moving plant; look out for overhead wires and electrical services including lights Have plant arm as low as possible at all times Minimum clearance from overhead services to be maintained at all times with a spotter utilized when required | 2M | Supervisor |
|  | Damage to surfaces | 2M | Inspect area of travel and be sure the surface is capable of taking the weight of the plant without damage | 1L | Supervisor |
|  | Overturn of plant | 3H | Never drive plant on wet sloping surfaces Never park plant on surface more than 20° Drive plant up and down never across a slope Stay clear of other plant and demolition works Never drive over or alongside trenches, cuttings or ravines/ditches | 2M | Supervisor |
| Step 4. Parking and securing |
| Completing work and leaving site | Damage to plant, theft or hazards | 3H | Equipment to be switched off and keys secured when plant not attended. Keys returned to site contact or client Attachments to be left on ground level. No loads to be left suspended from machine while unattended. Park plant in designated area clear of other hazards such as overhead wires, trenches, traffic areas | 2M | Supervisor |
|  | Fall from cabin | 3H | 3 points of contact at all times when access the truck bed and cabin Care must be taken in wet condition Safety footwear must be worn | 2M | Supervisor |
| Emergency situations |
| Emergency situations | Various | 4S | Stop work then follow the site evacuation instructions and notify emergency services if required. Determine evacuation assembly area during toolbox talk | 2M | supervisor |
| Reasonable adjustment to this SWMS |
| Performing the tasks in a way that does not reflect the above SWMS. Reasons: There is an omission from the SWMS You have to perform an extra task Performing the task as set out above may create a hazard |
| Task step: | Hazards: | Rating | Control of hazard | Rating after control | Responsible persons |
| Task step: | Hazards: | Rating | Control of hazard | Rating after control | Responsible persons |

| State Legislation (tick or add as applicable) |  |  |  |  |
| --- | --- | --- | --- | --- |
| Tick | Legislation | Tick | Codes of Practices/Guidance | Tick | Other |
|  | OHS Act 2004 - Vic |  | How to Manage Work Health & Safety Risks |  | Traffic Control at Work Sites – within each state |
|  | OHS Regulation - Vic |  | Hazardous Manual Tasks |  | Jaybro’s Procedures & Policies |
|  | Workplace Injury Rehabilitation and Compensation Act 2013 - VIC |  | Managing the risk of falls at workplaces |  | Temporary Fencing Installation manual |
|  | Environment Protection Act 1970 - VIC |  | Labelling of Workplace Hazardous Chemicals | Other relevant legislation |
|  | OHS Act 1984 -WA |  | Managing Noise &Preventing Hearing Loss at Work |  | Road Transport Act 2013 and Heavy Vehicle (Mass, Dimension and Loading) National Regulation 2013 |
|  | OHS Regulation 1996 - WA |  | Managing the Work Environment & Facilities | Australian and other Standards |
|  | Workers Compensation & Injury Act 1981 - WA |  | Work Health & Safety Consultation, Cooperation & Coordination |  | AS/NZS 2161.1 Occupational Protective glove |
|  | WHS ACT 2011 – NSW |  | First Aid in the Workplace |  | AS/NZS1337:1:2010 – Personal Eye and face protection |
|  | WHS Regulation 2011 - NSW |  | Construction Work |  | AS 2741-2002 1-2002 Shackles |
|  | Workplace Injury Management and Workers Compensation Act 1998 - NSW |  | Managing Risks of Hazardous Chemicals |  | Australian Standard AS2550—Cranes, hoists and winches—Safe use |
|  | Workers Compensation Regulation 2010 - NSW |  | Managing Risks of Plant in the Workplace |  | AS 4497.2-1997 Round slings - Synthetic fibre - Care and use |
|  | Protection of the Environment Operations Act 1997 - NSW |  | Cranes |  | AS/NZS 4801:2001 Occupational health and safety management systems |
|  | Work Health and Safety Act 2011 - QLD |  |  |  | AS/NZS 2210 (1980) Type 1 Safety Footwear |
|  | Work Health and Safety Regulation 2011 - QLD |  |  |  | AS 4687-2007 Temporary fencing and hoardings |
|  | Workers’ Compensation and Rehabilitation Act 2003 - QLD |  |  |  | AS NZS 1170.2-2011 Structural design actions - Wind actions |
|  | Workers’ Compensation and Rehabilitation Regulation 2014 - QLD |  |  |  |  |
|  | Environmental Protection Act 1994 |  |  |  |  |

Commitment Sign off

I, the undersigned, understand that;

| The SWMS has been explained to me Its contents are clearly understood by me My qualifications are current to undertake this activity – tick or note qualification | I have had the opportunity to have input into the preparation or adjustment of the SWMS I will comply with the SWMS otherwise work will stop immediately I understand the importance of and how to report incidents and near misses |
| --- | --- |

| Skills Matching + Consultation & Review Sign Off |
| --- |
| Training / Skill / Competency Required to Complete the Work Safely | White Card | Site induction | Crane license | First Aid | Forklift | Rigging | Dogging | Other | Other |
| All workers have been consulted, had an induction in and read and understand the requirements contained in this SWMS. Signed by ALL workers including non Orang Hire workers involved - Name and Signature: |  |  |  |  |  |  |  |  |  |
| NAME | SIGNATURE | DATE |  |  |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |
|  |  |  | ( | ( |  |  |  |  |  |  |  |

## Jaybro Group workers, contractors or sub-contractors must complete the below safety checklist with all other colleagues, offsiders and assistants to identify any hazards and state how they will control them.

| 1 | Stop, look and think | Yes | Action Required |
| --- | --- | --- | --- |
| Check with the team | Do all workers understand what they need to do? |  |  |
|  | Have SWMS been consulted, explained and Signed? |  |  |
|  | Permits obtained? (e.g. hot work/ground penetration etc.) |  |  |
|  | Are suitable and working tools/equipment available? |  |  |
|  | Is all PPE correct and fitted? |  |  |
|  | Are all workers trained and competent to perform this task? |  |  |
| 2 | Identify hazards – complete section 3 for controls of each hazard |  | What could happen? |
| Discuss if there are any of the following hazards | Manual handling (e.g. heavy lifting, awkward posture, impact or exertion) |  |  |
|  | Slips, trips and falls (e.g. from ladders, truck beds, platforms, elevated areas; debris, hoses, cables, uneven ground, wet areas etc.) |  |  |
|  | Mechanical (e.g. moving parts, moving plant, ejected objects) |  |  |
|  | Electrical (e.g. overhead wires, faulty tools, live power) |  |  |
|  | Chemical (e.g. inhalation, contact with acids, solvents, asbestos) |  |  |
|  | Pressure (e.g. contact with high pressure liquid or air) |  |  |
|  | Noise (e.g. loud noises, hearing emergency alarms or instructions) |  |  |
|  | Biological (e.g. exposure to potential disease carrying material) |  |  |
|  | Radiation (e.g. exposure to sunlight, UV or x-rays) |  |  |
|  | Psychological (e.g. stress, violence, fatigue) |  |  |
|  | Heat and Cold (e.g. working in hot or cold environments) |  |  |
| 3 | Controls for the above hazards |  |  |
| Hazard identified | Risk rating (low, medium, high) | How will you control the risk |
| 4 | Safe to proceed with work | ☐ Yes | ☐ No |